Encrypted ESP Ping
draft-antony-ipsecme-encrypted-esp-ping
Antony Antony <antony.antony@secunet.com>

---
IPsec Background
- IKE is control plane (UDP 500 or UDP 4500)
- ESP is Data plane (ESP or ESP-in-UDP 4500)

---
Problem Statement
- Diagnose ESP after IKE is established
- ESP packets do not share fate with IKE
- IKE might succeed but ESP packets are dropped
- Hard to detect and recover
- Data traffic is blackholed
- Why Not Use Existing IP Tools?

---
Why not ping over IPsec?
IPsec gateways has no IP from policy
eth0: 192.0.2.126/25
eth1: 192.0.2.252/25
eth0: 192.0.1.254/25
eth1: 192.1.2.23/24
pacifica
east
sunset
west
eth0
eth1
eth0
eth1
ESP
ESP
eth0
eth1
eth0: 192.0.2.254/25
eth1: 192.1.2.45/24
eth0: 192.0.2.125/25
xfrm policy 192.0.2.125/25 <-> 192.0.2.125/25
xfrm state 192.1.2.23 <=> 192.1.2.23 SPI 0xAABBCCDD
espping -s 0xAABBCCDD -I 192.1.2.45 192.1.2.23

---
Use cases
- Diagnose ESP Blocked or Filtered
- Probing Multiple ESP Paths to same end point
- Probe Return Path
  - ESP is two unidirectional Security Associations

---
Example
- espping -s <size> -I <src ip> [--spi <spi>] <dst ip>
- espping -I 192.1.2.23 –spi 0xAABBCCDD 192.1.2.45

---
Packet format : Request
IP Header
ESP
Protocol 50
Next Header 144
AGGFRAG_PAYLOAD
Sub-type (2) ESP-ECHO-REQUEST
R Flag
Data Length
Return Path SPI
Echo Payload
Identifier
Sequence #
Optional Data

---
Packet format : Response
IP Header
ESP
Protocol 50
Next Header 144
AGGFRAG_PAYLOAD
Sub-type (3) ESP-ECHO-RESPONSE
R Flag
Data Length
Return Path SPI
Echo Payload
Identifier
Sequence #
Optional Data

---
RFC 9347 CC Payload
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
Sub-type (1)
Reserved |P|E|
BlockOffset
BlockOffset
        LossEventRate
        RTT(22)
Echo Delay(21)
        Transmit Delay (21)
        TVal
        TEcho
DataBlocks ...

---
IP-TFC Congestion Control Payload
- CC payload helps to discover path properties:
  - One way delays,
  - loss rate.
  - estimated bandwidth
- Useful to probe manually even when IP-TFS is not negotiated

---
 IKEv2 Notify to announce support
Add IKEv2 Notification in -03 I.D.
ENCRYPTED_PING_SUPPORTED

---
SADB Implementation on receiver
- How to validate Return Path requested?
  - SADB is unidirectional
  - Especially when there are multiple SAs
  - Only IKEd knows the return path in its peer DB
  - Respond only to Paired SA?
  - Respond to all SA between same peer ?
    - Think of Fiber and Satellite backup path

---
Questions / Feedback?
Adoption?

---
Linux implementation

---
Linux: ESP Ping Socket
(similar to ICMP ping socket)
Encrypted ESP Ping socket
  - IPPROTO_ESPPING:
  - Send the payload and receive response.
    - Validate destination IP + SPI
    - Validate return source address + Return SPI

---
Implementation : Linux SADB?
- How to validate Return Path using SADB?
  - SADB is unidirectional
  - Simple a pair of SA is easy
  - Multiple SA between same pair (doable using peer DB)
  - SA over LTE and WiFi (may need external Daemon/IKEd)
- Sockets : Return response from other SPI
  - Based in Identifier in the payload, meta data (TTL, SPI,..)

---
Similar ideas
- MPLS LSP ping with return path : RFC 7110
- Bidirectional Forwarding Detection (BFD)
  - IP only (Not suitable for Encrypted ESP Ping)
  - https://www.rfc-editor.org/rfc/rfc8562

---
ESP Message